## Slide 1
Design in PIE coordinates
Compute a controller in the equivalent representation.
ODE–PDE model
PIE model
Convert
Implement K
STN–GPe
ASML
Canon
Analyze and synthesize
for the nominal linear dynamics.
Notes: The forward arrow is exact model conversion; the reverse arrow is controller implementation in the original physical coordinates. PIE methods provide computable operator conditions for analysis and synthesis of the nominal linear dynamics. The K block remains a generic controller with the same measured-signal and actuation ports as before. A controller synthesized in PIE state coordinates must be implemented using the state reconstruction/coordinate map; we do not claim a particular output-feedback structure is automatically convex. Delta is still in the full LFR: the nominal synthesis statement alone does not establish robust nonlinear closed-loop stability. The images are the user’s existing STN-GPe, ASML and Canon examples. PIETOOLS and PIE synthesis are discussed in the local paper introduction and preliminaries. Previous notes: Partial Differential Equations give a natural way to describe distributed systems, but stability analysis, observer design, and controller synthesis are challenging. Spatially distributed dynamics and boundary conditions complicate the application of large amount of theory that has been developed for ordinary differential equations. More recently, partial differential equations have been introduced as an alternative representation that brings much of the properties of ODEs to partial differential equations. Five steps PDE to PIE, 25

## Slide 2
Our first pillar: PIEs
An exact representation with tractable analysis and synthesis.
ODE–PDE model
PIE model
Convert
Implement K
STN–GPe
ASML
Canon
Pillar 1: tractability
PIE → LPI → LMI
Next: nonlinear stability and performance.
Notes: First pillar: exact PIE modeling plus PI-operator optimization provides tractability for the nominal distributed dynamics. The two diagrams and three application images keep exactly the same positions as slide 25. Morph preserves this visual bridge while the first-pillar conclusion appears and Delta becomes the next focus. Next we need a way to account for the nonlinearity/uncertainty and robust stability/performance; later duality enables the synthesis argument. This is not a claim that replacing PDE by PIE already solves the full uncertain nonlinear control problem.