## Slide 1
The shifted sigmoid lies in a sector
-400
400
0
STN activation about its equilibrium
Msc Defence T.M. Lenssen
1
Notes: The graph is the actual equilibrium-shifted STN activation used in the Parkinsonian simulation: phi(z)=M/2[tanh(2(zStar+z)/M)-tanh(2zStar/M)], M=300, zStar=-196.169333478339. Thus phi(0)=0. The horizontal and vertical equilibrium shifts must both be included. Global sector alpha=0, beta=0.734412133583743; the displayed beta is approximate, while the graph uses the full value. Beta is the maximum secant phi(z)/z, not the maximum derivative. The corresponding GPe channel has M=400, zStar=-285.173802460895, beta=0.704831466892149. The global lower sector bound is zero because this sigmoid saturates. Values come from the existing STN_GPe sector data; the local controller certificate is not used as a global bound.

## Slide 2
The sector gives two signed gaps
-400
400
0
STN activation about its equilibrium
Inside the sector, the two gaps have the same sign.
Msc Defence T.M. Lenssen
2
Notes: The upper and lower signed gaps are a=beta*z-w and b=w-alpha*z=w. The sector boundary lines pass through the shifted equilibrium (0,0). For z>0 the two gaps are nonnegative; for z<0 both are nonpositive. At zero, w=0 and both gaps vanish. The displayed filter simply computes these gaps; it does not replace the nonlinearity by a linear system.

## Slide 3
Transform the gaps into input and output
-400
400
0
STN activation about its equilibrium
Choose unit scaling: the transformed input depends only on z.
Msc Defence T.M. Lenssen
3
Notes: Choose the constant scaling s=1 in [[s,1],[s,-1]]. This s is not a Laplace variable or spatial coordinate. Then ztilde=a+b=beta*z and wtilde=a-b=beta*z-2w. Their squared difference is 4ab, nonnegative throughout the sector, so |wtilde|<=|ztilde|. Since beta>0, this defines the memoryless transformed map phitilde(v)=v-2phi(v/beta), with input v=ztilde and output wtilde. The original nonlinearity is still present.

## Slide 4
The transformed nonlinearity is dissipative
-400
400
0
STN activation about its equilibrium
Output energy cannot exceed input energy.
Msc Defence T.M. Lenssen
4
Notes: The transformed memoryless nonlinearity is dissipative with supply sigma=ztilde^2-wtilde^2=4ab and storage V identically zero. The supply is pointwise nonnegative, so its integral is nonnegative for every finite T>=0. For two channels, sum the channel supplies; for a spatial pointwise nonlinearity also integrate over space. These are mathematical input/output energy measures, not necessarily physical energy. No multiplier Pi or IQC formalism is needed for this explanation. Dissipativity of the isolated nonlinearity does not by itself prove stability of its feedback interconnection.