## Slide 1
Sector bounds describe Δ
Memoryless, acting at each spatial point
Every point of the nonlinear graph stays inside the sector.
Msc Defence T.M. Lenssen
1
Notes: A concrete static instance of Definition 5. Assume a real scalar memoryless pointwise operator w_Delta(t,s)=phi(z_Delta(t,s)), with phi(0)=0 and alpha<beta finite. The sector condition holds for every scalar input, time and spatial location. The graph is schematic: alpha=0.2, beta=1.2 and phi(z)=0.7*z+0.3*tanh(z). It illustrates the sector, not measured data. Both first and third quadrant wedges are shown. Sector membership is not the same as a bound on the derivative of phi.

## Slide 2
Sector bounds give a nonnegative supply
The two gaps have the same sign.
Their product is nonnegative.
For every input, at every time and spatial point.
Msc Defence T.M. Lenssen
2
Notes: The upper gap beta*z-w and the lower gap w-alpha*z have the same sign for a sector-bounded graph. At the positive input marked here both are nonnegative; for a negative input both are nonpositive. Their product q is nonnegative in both cases. q is a mathematical supply density, not necessarily physical heat or energy. The colours on the two factors match the two short gap segments in the diagram.

## Slide 3
Write the supply as a quadratic form
Msc Defence T.M. Lenssen
3
Notes: Expanding q gives -alpha*beta*z^2+(alpha+beta)*z*w-w^2. Thus the off-diagonal multiplier entries are (alpha+beta)/2. The matrix acts pointwise on the spatial channels; its entries represent scalar multiples of the identity operator on L2([a,b]). This multiplier is indefinite in general. x is defined here only to shorten the stacked input/output pair; all time and space arguments remain visible.

## Slide 4
Definition 5: a hard IQC for Δ
Use the sector multiplier in Definition 5.
Δ is dissipative with this supply and zero storage.
Msc Defence T.M. Lenssen
4
Notes: Because q(t,s)>=0 pointwise, integrating over the spatial domain and any finite time horizon gives a hard IQC. Choose Psi_Delta=I and the sector multiplier from the previous slide in Definition 5. Then the paper's truncated inner product is exactly this double integral. For this memoryless example choose nonnegative storage S identically zero, so S(T)-S(0)=0 <= integral q; hence Delta is dissipative with supply sigma(t)=integral_a^b q(t,s) ds. This does not assert that every dynamic IQC has zero storage or pointwise nonnegative supply. An IQC describing Delta alone is not a stability certificate for its feedback interconnection; a complementary plant condition is still needed. Reference: Megretski and Rantzer, System Analysis via Integral Quadratic Constraints, IEEE TAC 42(6), 1997, Section VI.I. https://services.montefiore.uliege.be/systems/grad04/megretski97.pdf